## Slide 1: Noise analysis of Spheroids
1/26/23
Daniel George
Bleris Lab

## Slide 2: Spheroid data
Slices: 115
  Analysis on 12-100
Fluorescence of cell line: CFP and mKate2
What was used:__

## Slide 3: Goal / hypothesis
Decompose total noise into extrinsic and intrinsic noise in a segmented fluorescence image of the spheroid
Hypotheses:
Cells in the outer layer of the spheroid are different than those in the inner layer in terms to their access to oxygen and nutrients.
Slices from the very top and bottom of the spheroid should consist mainly of cells from the outer layer.
Since extrinsic noise can be affected by access to oxygen and nutrients, there should be an increase in extrinsic noise as you progress towards the center.
Intrinsic noise should not change

## Slide 4: Process overview
1. Segmentation
2. Calculate mean for each segmented cell
3. Scatter plot for visualization
4. Intrinsic and extrinsic noise calculation

## Slide 5: 1. Segment
Cellpose algorithm (Stringer et al. Nature Methods 2021)
  Outputs the boundaries of different cells
Notes: Classical segmentation that was used involves the watershed algorithm which has to do with treating the image as a topological map and finding basins. Doesn’t work well with a lot of data because it is messy. This algorithm trained a modified U-net neural net to create an intermediary that is easier to segment. The intermediary is a vector flow representation of a simulated diffusion process. After they are combined, the gradient vector fields make a dynamical system where the pixels go to a fixed point. The pixels that all converge to a certain fixed point becomes a mask.
They also added an extra parameter to consider that different data types have different styles of segmentation.

## Slide 6: Segmentation example
Cellpose algorithm
  Outputs the boundaries of different cells
  Ex. frame 54

## Slide 7: Current segmentation workflow
Use GUI to
Find average cell diameter
Pick best pretrained network
Choose channel to create segmentation
Choose which segmentation has the most cells
Iterate through outlines of different cells and do statistical analysis on intensities

## Slide 8: 2. Mean intensity histogram
Notes: Higher CFP expression made it a better choice for being the one used to create the segmentation masks.

## Slide 9: 3. Scatter plot for visualization
Notes: If there are below a certain amount of cells, should I remove that frame as an outlier? Happens towards the beginning or end where a frame has 6 cells compared to the center which has about 30.
Make picture bigger.

## Slide 10: 4. Noise decomposition
Extrinsic noise
Intrinsic noise
Swain PS, Elowitz MB, Siggia ED. Intrinsic and extrinsic contributions to stochasticity in gene expression. Proc Natl Acad Sci USA. 2002
Notes: Use formula from https://authors.library.caltech.edu/74808/3/%5BStatistical%20Applications%20in%20Genetics%20and%20Molecular%20Biology%5D%20Estimating%20intrinsic%20and%20extrinsic%20noise%20from%20single-cell%20gene%20expression%20measurements.pdf; same as the one from Elowitz on the slides.
Elowitz: https://pubmed.ncbi.nlm.nih.gov/12237400/

## Slide 11: Intrinsic and extrinsic noise calculation
Notes: The ends of the extrinsic noise being high could be because the segmentation is circling ones that are all black as well as the middle one with high expression. The overall trend doesn’t seem to have changed with fixing the offset. RMS for best fit intrinsic. Split spheroid into half and combine. Extrinsic is cv. Intrinsic is RMS.

## Slide 12: Total noise
Notes: Overlay total noise and intrinsic and extrinsic

## Slide 13: Result
Hypothesis:
Since extrinsic noise can be affected by access to oxygen and nutrients, there should be an increase in extrinsic noise as you progress towards the center.

## Slide 14: Trends in extrinsic noise throughout the spheroid
The extrinsic noise increases as it progresses towards the middle and increases to a peak in the middle

## Slide 15: Limitations:
Segmentation quality varies based on CFP channel. If some part of the mKate2 segmentation is better, this information isn’t taken advantage of.
Notes: Plot number of points in each slice and look at data in each.

## Slide 16: Example of poor segmentation
Possible Extension:
Maximum disjoint set of segmentations

## Slide 17: Example of segmentation on 2D cell line
Note:
One channel must be DIC for the segmentation to work

## Slide 18: CV of expression vs Frame
Notes: Compare to total noise.
Single graph